## Slide 1
Dan and Alon
Planning in the Continuous Domain: a Generalized
Belief Space Approach for Autonomous Navigation in
Unknown Environments
Vadim Indelman, Luca Carlone , and Frank Dellaert
International Journal of Robotics Research - 2015
Indelman, V., Carlone, L., and Dellaert, F. (2014). Planning under uncertainty in the continuous domain: a generalized belief space approach. In IEEE Intl. Conf. on Robotics and Automation (ICRA).
Indelman, V., Carlone, L., and Dellaert, F. (2013). Towards planning in generalized belief space. In Proc. of the Intl. Symp. of Robotics Research (ISRR).

## Slide 2
Itinerary
Introduction
Terminology and General Belief Space Inference
Planning In the General Belief Space
Formulating Objective Function
Experimental Evaluation
Our Implementation
Possible Extensions
Notes: Total (25 min)
Introduction ----------- Alon (1:6) [2 min]
General Belief Space Inference (SLAM) ---------- Alon (7:11) [4 min]
Planning in the General Belief Space ----------- Dan (12:22) [6 min]
Formulating Specific Objective Function -----------Alon (23:29) [6 min]
Experimental Evaluation -----------Dan (30:36) [3 min]
Implementation -----------Alon(37) [1 min]
Possible Extensions -----------Alon(41) [3 min]

## Slide 3
Problem Statement
Formulate a general strategy to accomplish common tasks with the following assumptions:
Path Planning
Next Best View
Exploration
No prior knowledge of the environment
Continuous Domain (not discrete)
Maximum Likelihood Observations

## Slide 4
Approach:
Model Predictive Controller
Plan with the Estimation in mind – Reason about future observations

## Slide 5
Scenario:
UAV flies over an unknown region with a camera looking downwards.
Goal:
reach pre-specified goal positions while preserving an acceptable localization error
Notes: UAV in an unknown

## Slide 7
Terminology and General Belief Space Inference:
As the environment is unknown joint state vector
robot poses
landmarks
Gaussian models Gaussian posterior
Information Matrix
Estimation over the joint probability:
General belief
Motion model
Observation model

## Slide 8
– Mahalnobis norm
Prior
Motion Models
Observation models
Solving for the Posterior Distribution

## Slide 9
Linearize models around
Do this until convergence
The Gauss Newton Way
Solving for the Posterior Distribution

## Slide 10
of last iteration
Solving for the Posterior Distribution

## Slide 11
Solving for the Posterior Distribution
Whitened Jacobians
Whitened errors
Not a function of the measurements (at first iteration)

## Slide 12
Planning in the Generalized Belief Space
Estimate of future state

## Slide 13
Planning in the Generalized Belief Space
Past
Future

## Slide 14
Outer Layer: Updates given
Planning in the Generalized Belief Space
Inner Layer:
Computes given
Do this until convergence
Notes: Continuous Action Space:
The machine does not involve searching over the action space, but optimizing over it

## Slide 15
Outer Layer – Inference over the control
Updating via Gradient Decent:
or or
Convergence Criteria:
=
Discrete Gradient Computation:
Notes: (1) The control update is preformed in a continuous domain and can be realized using different optimization techniques. In the paper the method that used is a simple gradient method to compute .
(1) The control update is preformed in a continuous domain and can be realized using different optimization techniques. In the paper the method that used is a simple gradient method to compute 𝑢_(𝑘:𝑘+𝐿−1)^⋆.

## Slide 16
Inner Layer – Inference in GBS
Inner Layer:
Computes given
Outer Layer: Updates given
Past
Future
Notes: We Now know how to update u from J
No we need to learn how to compute J from u

## Slide 17
Inner Layer – Inference in GBS
To compute we need to infer in the future:
Complications Arise:
  Unknown if observation will be obtained
  Even if we have an observation, we cannot know what the measurement will be
Expectation Maximization
Notes: The inner layer involve the computation of the Gaussian approximation of:
Whose mean value coincides with the MAP estimate of:

## Slide 18
Inner Layer – Inference in GBS
(*Minka,1998)
Binary variable for each future observation (Acquired/Not Acquired)
Expectation Maximization
Notes: Minka 1998 promises that this EM convergences to a local minimum of the cost

## Slide 19
Also serves as linearization point
Inner Layer – Inference in GBS
Same process but with Whitened Jacobians
Notes: If “solving” EM without future measurements, we can find I_kpl_Bar

## Slide 20
Conditioning
Inner Layer – Inference in GBS
Motion model
Observation models
Prior
Notes: Finish slide with saying that we need to plug in the models and then we get -> next slide

## Slide 21
Inner Layer – Inference in GBS

## Slide 23
A specific Family of Objective Functions
penalizes control effort
Penalizes pose uncertainty
Penalizes last poses’ uncertainty
Penalizes last poses’ distance from goal
- Weight Matrices
- Selection Matrices

## Slide 24
A specific Family of Objective Functions
Not a function of measurements
From term
Not a function measurements under 1 Newton-Gauss Iteration

## Slide 25
A specific Family of Objective Functions
Falls if assuming maximum likelihood measurements
Contains the matrix Rewards loop closures

## Slide 26
Choice of
The Larger the smaller the control efforts.
smaller control efforts less torque applied to turn
Notes: The lar

## Slide 27
Choice of and
Selection Matrix
Selection Matrix
Last poses’ covariance

## Slide 28
Choice of and
can’t be bigger than 1

## Slide 29
Proposed method for
Choice of and
Naïve approach to choose

## Slide 30
Experimental Evaluation
Statistical Study (Uniform)
Different Planning Horizons (clusters)
Comparison to related work
Uniform
Oasis
Clusters
Implementation via GTSAM

## Slide 31
Statistical Study in “Uniform” Environment
30 runs with different noise realizations
Smooth trajectories
Similar loop closure events (pose Index == 100)
Estimation errors are below the square root covariance trace

## Slide 32
Experimental Evaluation – Horizon Length
Longer horizon makes for better planning but with a significant cost to computation time

## Slide 33
Experimental Evaluation – Method Comparison
Notes: CNU – Continuous Planning no uncertainty
DP - Discrete Planning:
Selects a set of waypoints that corresponds to a potential loop closure location and calculates a path using global Astar.
Uses a heuristic to reward nodes where the robot is likely to reobserve landmarks
Uses cost with two contrasting objectives: minimizing uncertainty and exploring new areas

## Slide 34
Experimental Evaluation - Uniform
CNU goes in straight lines and ignores uncertainty (expected)
CNU produces the largest estimation error (expected)
GBS and GBS-ML are very similar in performance
Planning time in GBS and GBS-ML increase when turns are required (more iterations in gradient decent)
Discrete approach is also able to produce plan that satisfies soft uncertainty
Discrete approach control effort is a-lot more significant (‘zig zag’ actions)

## Slide 35
Experimental Evaluation - Oasis
Summarization:
CNU is ‘cheap’ but produces large estimation error
GBS and GBS-ML are very similar in performance
GBS and GBS-ML computations increase when turning
Discrete approach has high control effort

## Slide 36
Experimental Evaluation - Clusters
Summarization:
CNU is ‘cheap’ but produces large estimation error
GBS and GBS-ML are very similar in performance
GBS and GBS-ML computations increase when turning
Discrete approach has high control effort

## Slide 37
Parameter List
– robot FOV
– robot range
– motion covariance
– measurement covariance
– gradient decent eps
– gradient decent learning rate
- gradient decent max iterations
- control effort weight
– covariance limit
- logic controller
<default isam2 parameters>

## Slide 38
Deliberation and Possible Extensions - Weights
Assumptions:
Myopic setting
Linear motion model:
Notes: Due to quadratic cost:
  we apply very strong control actions (arbitrarily neglecting the nominal control, while, close to the goal, we apply weak control and we
  mainly follow the nominal control)
Weighting quadratic costs is difficult and was handled via a changing alpha value.
We can also:
Set waypoints to make the term Xg-Xk constant
Use l1 norm instead of Euclidian norm for distances (removes the dependence of the control action on the distance to the goal but is not differentiable at the origin and yada yada)

## Slide 39
Deliberation and Possible Extensions – Loopy Solutions
Sometimes a goal is just out of reach….
Dynamically relax ?

## Slide 40
Deliberation and Possible Extensions – Hard constraints
(1)
(2)
Notes: Instead of penalizing violation from the bounds, make sure in a hard constraint that we don’t violate. This will guarantee that we don’t “skew”
When x -> 0 log(x) -> -inf making the cost basically inf.

## Slide 41
Deliberation and Possible Extensions – Other ideas
Obstacle Avoidance
Efficiency:
Exact Differentials with Lie Algebra
Smart Initialization
Smarter numerical optimization
than vanila gradient decent
Earlier actions have more effect. Optimize less on later actions
Adaptive Horizons
Simplifications
Notes: Adaptive Horizon length: Check distance to goal before deciding
Simplifications: (image from khen Elimelech and Vadim “Simplified decision making in the belief space using belief sparsification”
Solver
Cluster of landmarks -> one landmark