## Slide 1
Dan and Alon
Planning in the Continuous Domain: a Generalized
Belief Space Approach for Autonomous Navigation in
Unknown Environments
Vadim Indelman, Luca Carlone , and Frank Dellaert
International Journal of Robotics Research - 2015
Indelman, V., Carlone, L., and Dellaert, F. (2014). Planning under uncertainty in the continuous domain: a generalized belief space approach. In IEEE Intl. Conf. on Robotics and Automation (ICRA).
Indelman, V., Carlone, L., and Dellaert, F. (2013). Towards planning in generalized belief space. In Proc. of the Intl. Symp. of Robotics Research (ISRR).

## Slide 2
Problem Statement
Formulate a general strategy to accomplish common tasks in robotics in the following setting:
No prior knowledge
Continuous Domain (as opposed to discrete)
Maximum Likelihood Observations
Path Planning
Next Best View
Exploration

## Slide 3
Approach:
Model Predictive Controller
Plan with the Estimation in mind

## Slide 4
Motivating Example Used:
UAV flies over an unknown region with a camera looking downwards.
Its goal is to reach pre-specified goal positions while preserving an acceptable localization error
Notes: UAV in an unknown

## Slide 6
Plan with Estimation in Mind:
As the environment is unknown, a joint state vector is held:
robot poses
landmarks
Estimation over the joint probability:
Motion model
Observation model
Architect models such that the posterior can be modeled as a gaussian:
Information Matrix

## Slide 7
Solving for the posterior distribution via Expectation Maximization:
Prior
Motion Models
Observation models

## Slide 8
Linearize models around
Do this until convergence
Solving for the posterior distribution via Expectation Maximization:

## Slide 9
Solving for the posterior distribution via Expectation Maximization:
Whitened Jacobians
Whitened errors
Not a function of the measurements (at first iteration)

## Slide 10
Solving for the posterior distribution via Expectation Maximization:
Do this until convergence

## Slide 11
Planning in the Generalized Belief Space
Estimate of future state

## Slide 12
Planning in the Generalized Belief Space
Past
Future

## Slide 13
Planning in the Generalized Belief Space
Inner Layer:
Computes given
Outer Layer: Updates given

## Slide 14
Outer Layer – Inference over the control
Updating via Gradient Decent:
    - is the gradient of the objective function
    – suitable step size (positive value)
Convergence Criteria: or or
=[]
Notes: (1) The control update is preformed in a continuous domain and can be realized using different optimization techniques. In the paper the method that used is a simple gradient method to compute .
(1) The control update is preformed in a continuous domain and can be realized using different optimization techniques. In the paper the method that used is a simple gradient method to compute 𝑢_(𝑘:𝑘+𝐿−1)^⋆.

## Slide 15
Planning in the Generalized Belief Space
Inner Layer:
Computes given
Outer Layer: Updates given

## Slide 19: Planning in the GBS
At planning time , the optimal control minimizes an objective
) for look ahead steps:
  reminder:
  The objective involves immediate cost functions , one for each look-ahead step.
  The subscript in to remark that the objective function depends on the generalized belief at planning time

## Slide 20: Planning in the GBS
We can see in the objective that the expectation is taken to account for all the possible observations during the planning lag. Since these are not given at planning time and are stochastic, each immediate cost function may involve ant subset of states
Therefore, the immediate cost can be written as:

## Slide 21: Planning in the GBS
The expectation is a linear operator so we can rewrite the objective function as:
In order to optimize the objective function ,as written in the paper, we resort to an iterative optimization approach, starting from known initial guess on the controls.

## Slide 22: Planning in the GBS
The problem addressed in the paper is to find the optimal control policy:
Calculating the optimal control policy involves the optimization of the objective function

## Slide 23: Planning in the GBS
The optimization approach can be described as a dual-layer inference:
  The inner layer preforms inference to calculate the generalized belief at each of the look ahead steps for given
  The outer layer preforms inference over the control minimizing the objective function
  Since the computation of the optimal control relies on the computation of the generalized belief, we refer to our approach with the term generalized belief space (GBS) planning.

## Slide 25: Outer Layer: Inference over the control
Planning in the GBS

## Slide 26: Planning in the GBS
In order to finding a locally-optimal control policy corresponds to minimizing the general objective function:
The outer layer is an iterative optimization over the non- linear objective function Like we mentioned in the optimization starts from a nominal control and at each iteration, computes the delta vector that is used to update the current values of the controls:
Outer Layer: Inference over the control

## Slide 27: Outer Layer: Inference over the control
The control update is preformed in a continuous domain and can be realized using different optimization techniques. In the paper the method that used is a simple gradient method to compute .
Gradient Descent Method: At each i-th iteration of this method the current control is updated as follows:
  Where:
    - is the gradient of the objective function
    – suitable step size (positive value)
The iterations terminate when a suitable stopping condition is reached.
One common stopping condition are based on the norm of the
(the gradient become zero at minimum).
Planning in the GBS

## Slide 28: Outer Layer: Inference over the control
upon convergence the gradient method provides the optimal control policy for look-ahead steps.
according to the standard model predictive control framework at each time the agent solve the optimization problem and only applies the first command extracted from the computed policy
Planning in the GBS

## Slide 29: Inner Layer: Inference in GBS
Planning in the GBS

## Slide 30: Inner Layer: Inference in GBS
Planning in the GBS
The inner layer involve the computation of the Gaussian approximation of:
Whose mean value coincides with the MAP estimate of:
Number of complications arising when trying to solve the problem:
  Unknown if observation will be obtained
  Even if we have an observation we cannot know a-priori what the future measurement will be

## Slide 31: Inner Layer: Inference in GBS
Planning in the GBS
  The complications lead to definition of 2 new random variables:
  1. - observation at time of the th landmark
  2. - random variable for each observation (acquired or not acquired)
  and lead to a new joint probability density:
  Noted that being the number of possible observations at time
  Using chain rule, we can write the joint probability as:
Notes: 1.In our mobile robotics example, is simply the number of landmarks
observed thus far
1.In our mobile robotics example, 𝑛_𝑖 is simply the number of landmarks
observed thus far

## Slide 32: Inner Layer: Inference in GBS
Planning in the GBS
  The complications lead to definition of 2 new random variables:
  1. - observation at time of the th landmark
  2. - random variable for each observation (acquired or not acquired)
  and lead to a new joint probability density:
  Noted that being the number of possible observations at time
  Using chain rule, we can write the joint probability as:
  Using the assumption that the prior is un-informative we can write the probability as:
Notes: 1. We now take the assumption that the prior is uninformative.
This assumption is fairly standard in inference, see, e.g., Eq. (2.55)
in (Thrun et al., 2005)).
1. We now take the assumption that the prior 𝑝 (𝑍_(𝑘+1:𝑘+𝑙) |𝑍_𝑘, 𝑈_(𝑘−1, 𝑢𝑘:𝑘+𝑙−1)) is uninformative.
This assumption is fairly standard in inference, see, e.g., Eq. (2.55)
in (Thrun et al., 2005)).

## Slide 33: Inner Layer: Inference in GBS
Planning in the GBS
  We want to compute the belief which defined only over the states, we marginalize the random variables and get:
  Although the expression above can be used to compute the MAP estimator, there are 2 issues are still on the way:
  1. Marginalize is intractable is general
  2. The predicted belief is a function of which are unknown at planning time
  Therefore, rater than computing a single vector representing the MAP estimate, here the objective is to compute a vector-valued function of which gives the MAP estimate for each possible value of .
  The paper solve these two complications exploiting with two tools, expectation-maximization and Gauss-Newton approach.
Notes: 1.

## Slide 34: Inner Layer: Inference in GBS
Planning in the GBS
  According to the expectation-maximization (EM) approach instead of minimizing directly the probability which requires to marginalize we minimize the following:
  Where the expectation is computed assuming a given nominal state
Notes: 1.

## Slide 35: Planning in the GBS
  Illustration of the dual-layer inference planning approach:

## Slide 36: Outer Layer: Inference over the control
Gradient descent simulation
Planning in the GBS

## Slide 37: Objective functions
The exposition thus far has been given for general immediate cost function
Now when taking about the state its include the robot trajectory (collection of poses), and 3D positions of landmarks in the environment
In the paper the agent is a UAV and in each time step there are three main objectives:
  Reach a given goal position
  Keep its position estimate uncertainty below a given bound
  Has to minimize control usage

## Slide 38: Objective functions
According to the requirements in the last slide the paper design the following family of immediate costs:
where:
1. are wight matrices
2. is some known function that, depending on the application, quantifies the usage of control

## Slide 39: Objective functions
Reminder that our general objective function form is:
Plugging the 2 equations from the previews slide into the objective form we get:
Denote that the expectation removed from the first and the second summand as they do not depend on

## Slide 40: Objective functions
After computing the expectation in the last summand in the objective function in the previews slide, the objective function get the form:
Where the term (a) contains term penalizing control usage; the term (b) contains terms penalizing uncertainty, and the term (c) represents the expected inventive in reaching the goal.

## Slide 41: Objective functions
In the final objective term, we saw that we have three weight matrices and now we will discuss how to properly choose them.
Choice of This matrix has a very intuitive function. A large induces more conservative policies that penalize large controls. In the paper scenario, the control usage quantifies the change in the yaw angle;, which is used by the UAV to control the direction of its motion. In the demonstrated Figure, from the paper below, we can see that higher values of lead to smoother movement (apply smaller force to change the yaw angle). In the figure the goal is to move from the red point to each of the points 1,3,5,7 and then go back to the start position.
Implementation Details